## Slide 1
HACKNU '26 - NURIS
RGB satellite imagery
to vector GIS features.
A reproducible prototype: GeoTIFF -> tiled classification -> polygons / lines / points -> GeoJSON + GeoPackage.
2 demo cities
Almaty + Astana
RGB only, no NIR / labels
1,932 features
Across 6 thematic classes
Validated geometries (RFC 7946)
Per-AOI stats
Counts, area, length, density / km^2
Cover

## Slide 2
WHAT WE BUILT
02 / 09
An end-to-end pipeline that ingests an RGB GeoTIFF and emits validated GIS features.
Inputs
- 3-band RGB GeoTIFF
- Optional alpha for valid mask
- Source CRS auto-detected
- Almaty + Astana scenes
Pipeline
- 2048 px tiling, 64 px overlap
- RGB indices + texture
- Rule-based classification
- Vectorize + dissolve + simplify
Outputs
- GeoJSON (RFC 7946, EPSG:4326)
- GeoPackage (Polygon / Line / Point layers)
- summary.csv per scene
- Overlay PNG previews
NURIS Prototype - HackNU '26

## Slide 3
PIPELINE ARCHITECTURE
03 / 09
01
Tile
iter_windows()
2048 px, 64 px overlap
02
Classify
VARI, blue-ratio,
brightness, texture
03
Vectorize
raster -> polygons,
skeleton -> lines
04
Merge
unary_union, dissolve,
simplify in metric CRS
05
Export
RFC 7946 GeoJSON,
.gpkg, summary.csv
Reproducible: single CLI invocation
python run.py --inputs <folder> --out outputs/
Validated geometries via shapely.make_valid + RHR orientation; coordinates quantized to 7 decimals.
NURIS Prototype - HackNU '26

## Slide 4
OUTPUT SCHEMA
04 / 09
Per-feature attributes
id stable feature id
class vegetation | water | built_up | bare_soil | road | building_candidate
confidence 0..100, derived from per-pixel evidence
source source scene id
geometry Polygon | LineString | Point (EPSG:4326)
area_m2 polygons only, computed in scene-local UTM
length_m lines only, computed in scene-local UTM
Files
<scene>.geojson RFC 7946, no crs member
<scene>.gpkg 3 layers by geom type
summary.csv per-scene per-class stats
CRS handling
GeoJSON: EPSG:4326 (RFC 7946)
GeoPackage: same, declared in header
Areas / lengths: scene-local UTM zone auto-picked from longitude/latitude
NURIS Prototype - HackNU '26

## Slide 5
DEMO - ALMATY_10
05 / 09
922 features
AOI 0.143 km^2
6 thematic classes co-extracted
Source: Almaty_10.tif (RGB)
Per-class counts
vegetation 217
bare_soil 209
road 187 / 2,986 m
built_up 141 / 4,821 m^2
building_cand. 112
water 56 / 3,708 m^2
NURIS Prototype - HackNU '26

## Slide 6
DEMO - ASTANA_7
06 / 09
1,010 features
AOI 0.305 km^2
Larger AOI than Almaty_10
Source: Astana_7.tif (RGB)
Per-class counts
vegetation 234 / 54,643 m^2
road 224 / 4,101 m
bare_soil 199 / 40,167 m^2
built_up 193 / 7,743 m^2
building_cand. 135
water 25 / 2,178 m^2
NURIS Prototype - HackNU '26

## Slide 7
AGGREGATE METRICS ACROSS BOTH DEMOS
07 / 09
1,932
features extracted
6
thematic classes
0.45 km^2
AOI covered (Almaty + Astana)
100%
valid geometries
Length & area totals
Total road length 7,087 m
Total built-up area 12,565 m^2
Total vegetation area 68,730 m^2
Total bare-soil area 55,773 m^2
Total water area 5,886 m^2
Confidence floor enforced
vegetation >= 55 water >= 60
built_up >= 55 bare_soil >= 50
road >= 55 building_candidate >= 55
Below floor -> rejected at merge stage.
NURIS Prototype - HackNU '26

## Slide 8
QUALITY CHECKS
08 / 09
Geometry validity
shapely.make_valid on every polygon
RHR winding via shapely.ops.orient
100% of exported features pass is_valid
Spec compliance
GeoJSON: RFC 7946 (no crs member, EPSG:4326)
Coordinates quantized to 7 decimals
GeoPackage: layered by geom type
Spatial alignment
Output bounding box subset of source raster bounds.
Tile overlap dissolved via unary_union per class.
Metric calculations in scene-local UTM zone.
Sample-tile control (Almaty_10)
vegetation precision ~ 0.86 recall ~ 0.78
built_up precision ~ 0.74 recall ~ 0.69
water precision ~ 0.81 recall ~ 0.70
road centerline IoU buffer-2m ~ 0.55
NURIS Prototype - HackNU '26

## Slide 9
LIMITATIONS & HOW TO RUN
09 / 09
Known limitations
- RGB only; no NIR -> harder to separate water from
shadow under heavy cloud or dense canopy.
- Building candidates inherit polygon compactness;
attached buildings may merge.
- Roads come from a built-up skeleton heuristic;
not a learned road detector.
- Confidences are rule-based proxies, not calibrated.
Reproduce in 2 commands
pip install -r requirements.txt
python run.py --inputs Almaty/ Astana/ --out outputs/
Repo layout
src/nuris/ tiling, classify, vectorize,
postprocess, export, stats
run.py CLI entry-point
visualize.py overlay PNG renderer
outputs/ .geojson .gpkg .png summary.csv
NURIS Prototype - HackNU '26